## Slide 1: Block Device Driver Presented by :Aishwarya Deshmane

## Slide 2: Contents :
What is block driver?
How block device driver works?
Writing a block device driver.
File operation.

## Slide 3: What is Block Driver?
Devices that support a file system are known as block devices.
Driver written for these devices are known as a block device drivers.
Block device drivers take a file system request, in the form of a buffer structure, and issue the I/O operation to the disk to transfer the specified block.

## Slide 4: Module initialization and exit
The initialization and exit function of the sample block driver
Is similar to the normal driver.
Module_init(sampleblk_init) ;
Module_exit(sampleblk_exit);

## Slide 5: Sampleblk_init
Initialization function does the following things:
Block device registration
Allocation and initialization of driver state data structure.
Disk creation and initialization

## Slide 6: Block devices Registration :
The first step in the initialization of a block device driver is the registration of the major number
int register_blkdev(unsigned int major, const char *name);
Major can be 0, in which case it is dynamically allocated Once registered, the driver appears in /proc/devices with the other block device drivers
At cleanup time, the major must be unregistered void
unregister_blkdev(unsigned int major, const char *name);
The prototypes of these functions are in <linux/fs.h>

## Slide 7: Allocation and initialization of driver state data structure:
The driver declare a data structure to store states information that driver needs and can access frequently.
  Struct sampleblk_dev{
  Int minor,
  Spinlock_t lock;
  Struct request_queue *queue;
  Short media_changed;
  Struct gendisk *disk;
  Unsigned int size;
  Void *data
  }

## Slide 8: Struct gendisk :
Defined in <linux/genhd.h>
int major.
int first_minor.
int minors.
struct block_device_operations *fops.
struct request_queue *queue.
sector_t size.
Spinlock_t lock.

## Slide 9: Allocation of the disk :
Allocate a gendisk structure
struct gendisk *alloc_disk(int minors)
minors tells the number of minors to be allocated for this disk. Usually 1, unless your device can be partitioned.

## Slide 10: Initializing the disk :
Set the capacity
void set_capacity(struct gendisk *disk, sector_t size)
Add the disk to the system
  void add_disk(struct gendisk *disk);
The block device can now be accessed by the system, so the driver must be fully ready to handle I/O requests before calling add_disk(). I/O requests can even take place during the call to add_disk().

## Slide 11: Unregister the device:
Unregister the major number
  unregister_blkdev(unsigned int major, const char *name);
Unregister the disk
  void del_gendisk(struct gendisk *gd);

## Slide 12: File Operation :
1) Open and Release Method:
They are called whenever the devices is opened and closed.
The open method looks very similar to its char-driver equivalent ; it takes the relevant inode and file structure pointers as arguments. Where the inode refers to the block devices. Struct file is a pointer to Structure file.(It is a pointer to file object).
int (*open)(struct inode *inode, struct file *filp);
int (*release)(struct inode *inode, struct file *filp);

## Slide 13
2) Media_changed and Revalidate:
The block_device_operations structure includes two methods for supporting removable media. If you are writing a driver for a non removable device, you can safely omit these methods.
Their implementation is relatively straightforward.
The media_changed method is called (from check_disk_change) to see whether
the media has been changed; it should return a nonzero value if this has happened. The implementation is simple; if the media changed a flag that has been set :
int media_changed(struct gendisk *gd)

## Slide 14
2) Media_changed and Revalidate :
The revalidate method is called after a media change; its job is to do whatever is required to prepare the driver for operations on the new media, if any. After the call to revalidate, the kernel attempts to reread the partition table and start over with the device. The implementation simply resets the media_change flag and zeroes out the device memory to simulate the insertion of a blank disk.
int revalidate(struct gendisk *gd)

## Slide 15
3) Request method :
This core of every block driver is its request function. The function is called whenever the kernel believes it is time for your driver to process some read , write or the other operations on the devices.
void request(request_queue_t *queue);
Every device has request queue. Request_queue is created by the kernel when ever a device is connected.
dev->queue =blk_init_queue(request, &dev->lock);
Above function initialize memory for the request queue.
Arguments of this function are pointer to the request function and the spinlock as a part of queue creation process. Whenever the request function is called, that lock is held by kernel. So that the request function is running in atomic context.
To return a request queue to the system (at module unload time, generally), call(blk_cleanup_queue):
void blk_cleanup_queue(request_queue_t *);

## Slide 16
4) Transfer :
The driver can implement the actual data transfer using memcpy as the data is already in memory after all. The function that performs this copy operation is
(transfer ). It also handles the scaling of sector sizes and ensure that we do not try to copy beyond the end of our virtual device.
void transfer(struct dev *dev, unsigned long sector, unsigned long nsect, char *buffer, int write/Read)

## Slide 18
Thank you