Goal
- Create device number
- Create device files
- Make a char device registration with the VFS (CDEV_ADD)
- Implement the driver’s file operation methods for open, read, write,

---
Major and Minor Numbers
- Major numbers
  - Major number identifies the driver associated
    with the device
  - Char drivers are identified by a c
    - crw------- 1 root root 5, 1 Apr 12 1650
  - Block drivers are identified by a b
    - brw-rw---- 1 awang floppy 2, 0 Apr 12 1650
- Minor numbers
  - Minor number is used by the kernel to determine
    which device is being referred to

---
The Internal Representation of Device Numbers
- dev_t type, defined in linux/kdev_t.h
- 12 bits for the major number
  - Use MAJOR(dev_t dev) to obtain the major number
- 20 bits for the minor number
  - Use MINOR(dev_t dev) to obtain the minor number
- Use MKDEV(int major, int minor) to turn them into a dev_t

---
Statically Allocating Device Numbers
- To obtain one or more device numbers, use
- int register_chrdev_region(dev_t first, unsigned int count, char name)
- Returns 0 on success, error code on failure
- first
  - Beginning device number
  - Minor device number is often 0
- count
  - Requested number of contiguous device numbers
- name
  - Name of the device

---
Dynamically Allocating Device Numbers
- Kernel can allocate a major number on the fly
- int alloc_chrdev_region(dev_t dev, unsigned int firstminor, unsigned int count, char name)
- dev
  - Output-only parameter that holds the first number on success
- firstminor
  - Requested first minor number often 0

---
Freeing Device Numbers
- To free your device numbers, use
- int unregister_chrdev_region(dev_t first,unsigned int count)
- first
  - Beginning device number
  - Minor device number is often 0
- Count
  - Requested number of contiguous device numbers

---
Char Device Registration
- Need to allocate struct cdev to represent char devices
- include linux/cdev.h
- Need to initialize file_operations and
- set owner to THIS_MODULE
- Runtime
  - struct cdev * my_cdev = cdev_alloc()
  - my_cdev-> &my_fops (fops:struct file_operations )
- Own allocation
  - void cdev_init(struct cdev *cdev, struct file_operations *fops)

---
Char Device Registration
Inform the kernel by calling
int cdev_add(struct cdev cdev, dev_t num,unsigned int count)
  - Cdev : struct cdev variable
  - Num : first device number
  - Count : number of device numbers
- After this function call, the kernel knows the association between the
  major/minor numbers and the file operation.your device is ready to be used
- Remove a char device, call this function
  - void cdev_del(struct cdev dev)
    - Cdev : struct cdev variable

---
Device File Creation
- Manually device file creation
  - Mknod -m <permission> <name> <device type> <major > <minor>
  - Eg . Mknod -m 666 /dev/char_device c 250 2
- Dynamic device file creation
  - Include the header file linux/device.h and linux/kdev_t.h
  - Create the struct Class
  - Create Device with the class which is created by the above step
  Create the class
- Create a directory in sysfs : /sys/class/<your_class_name>
- struct class * class_create(struct module *owner, const char *name);
  - owner – pointer to the module that is to “own” this struct class
  - name – pointer to a string for the name of this class
- the pointer created here is to be destroyed when finished by making a call to class_destroy.
  - void class_destroy (struct class * cls);

---
Device File Creation
Create Device
- This function creates a subdirectory under /sys/class/<your_class_name> with your device name.
- This function also populates sysfs entry with dev file which consists of the major and minor numbers, separated by a : character
  - /sys/class/your_class_name/your_device_name/dev
- struct device *device_create(struct *class, struct device *parent, dev_t dev, void * drvdata, const char *fmt, ...);
- class – pointer to the struct class that this device should be registered to
- parent – pointer to the parent struct device of this new device, if any
- devt – the dev_t for the char device to be added
- drvdata – the data to be added to the device for callbacks
- fmt – string for the device’s name
- ... – variable arguments

---
File Operations
- The file_operation structure ste up operation that applies to the reserved device number
- It is defined in <linux/fs.h>
- A collection of function pointer.
- In this character driver we will give support to handle the below user level system calls
  - open
  - close
  - read
  - Write

---
File Operations

---
File Operations
- int (open) (struct inode *inode, struct file *file);
  - Return :0 if open is successful Negative error code if open fails
- first operation performed on the device file
- int (release) (struct inode *inode, struct file *file);
  - Return :0 if open is successful Negative error code if open fails
- ssize_t (read) (struct file * file, char __user * buff, size_t count, loff_t * f_pos )
  - returns the number of bytes read, or anegative value/
    appropiate error code on errors
  - File : Pointer of file object
  - Buff : Pointer of user buffer
  - Count : Read count given by user
  - f_pos : Pointer of current file position from which theread has to begin

---
File Operations
- ssize_t (write) (struct file *, const char _ _user *, size_t, loff_t *);
  - returns the number of bytes read, or anegative value/
  - appropiate error code on errors
  - File : Pointer of file object
  - Buff : Pointer of user buffer
  - Count : Read count given by user
  - f_pos : Pointer of current file position from which theread has to begin
File operation defination example
static struct file_operations fops =
{
.owner = THIS_MODULE,
.read = etx_read,
.write = etx_write,
.open = etx_open,
.release = etx_release,
};

---
Copy data between user space and kernel space.
- Using this driver we can send strings or data to the kernel device driver using the write function. It will store that string in the kernel space.

---
copy_from_user
- unsigned long copy_from_user (void *to, const void *from, unsigned long count);
  - to – Destination address, in the kernel space
  - from – The source address in the user space
  - count – Number of bytes to copy

---
Copy data between user space and kernel space
- Then when I read the device file, it will send the data which is written by write by function to the userspace application.

---
copy_to_user
unsigned long copy_to_user (void *to, const void *from, unsigned long count);
  - to – Destination address, in the user space
  - from – The source address in the kernel space
  - count – Number of bytes to copy

---
Memory created and deleted for kernel buffer
- kmalloc function is used to allocate the memory in kernel space
- The function is fast and doesn’t clear the memory it obtains.
- #include <linux/slab.h>
- void *kmalloc(size_t size, gfp_t flags);
  - size– how many bytes of memory are required.
  - flags– the type of memory to allocate.
The flags argument may be one of:
  - GFP_USER – Allocate memory on behalf of the user. May sleep.
  - GFP_KERNEL – Allocate normal kernel ram. May sleep.
  - GFP_NOIO – Do not do any I/O at all while trying to get memory.
  - GFP_NOFS – Do not make any fs calls while trying to get memory.
  - _GFP_HIGH – This allocation has high priority and may use emergency pools.
  - __GFP_NOFAIL – Indicate that this allocation is in no way allowed to fail (think twice before using).
  - __GFP_NORETRY – If memory is not immediately available, then give up at once.
  - __GFP_NOWARN – If allocation fails, don’t issue any warnings.
  - __GFP_REPEAT – If allocation fails initially, try once more before failing.

---
Memory created and deleted for kernel buffer
- This is like a free() function in the userspace. This is used to free the previously allocated memory.
- void kfree(const void *objp)
  - *objp – pointer returned by kmalloc